## Slide 1: Bharat Patel M.Sc.
Senior Network Architect
Nodes

## Slide 2
What are Nodes?
Device which converts optical signals delivered over fibres
to electrical (RF) signals to be delivered over coaxial cables on the
Down stream and converting electrical to optical on the Upstream. It is one of the important parts which make the network a “Hybrid” network - HFC
Node is also referred to as the area or segment of an HFC network
e.g. 500 home node or 2000 home node etc.

## Slide 3: Headends and nodes
ATMux
ATMux

## Slide 4
Main Headend
Subscriber management
BXX
ACX
ACX
DXX
CXE
DXE
Regional Headend
CATVisor
Fibre 1310 / 1550 nm
Network Element Management
Coax Network
House Network
Fibre node
DVX
Internet Proxy Server
Local services NVOD etc.
Internet
Headend
DVX
Headend
DVX
Fibre Backbone
ATM / SDH / IP
New Services VOD etc.
Internet Proxy Server
VoIP Gateway
PSTN
Network management
Cable modem
Set Top Box /
Cable modem
TV
Cable
phone
PC
Subscriber

## Slide 5: 2000 Home Segment/Node
M
500 homes
500 homes
500 homes
500 homes
Node
N Km
Headend
Fibre Link
Coaxial Network
Optical – Electrical Gateway and Point of congestion

## Slide 6: 500 Home Segment/Node
500 homes
500 homes
500 homes
500 homes
Headend

## Slide 7: 500 Home Segment/Node
M
150 homes
100 homes
120 homes
100 homes
Node
N Km
Headend
Fibre Network
Coaxial Network
Optical – Electrical Gateway and Point of congestion

## Slide 8: 125 Home Segment/Node
150 homes
120 homes
100 homes
100 homes
Headend

## Slide 9: Fibre node platforms
Fully modular node with full functionality and 4 active outputs
Compact node with
basic functionality
FTTH node
BXX
AC8000
CXE800
RN1000
Compact node with 2
active outputs and
high modularity

## Slide 10: BXX Platform
Notes: This slide shows Telestes modular, intelligent fibre node which allowes the full migration from single node to dual node application.
2 optical receivers, 2 return transmitters, 4 active high level rf-outputs, two redundant power supplies, separate place for fibre management, weather proof housing, advanced configuration/monitoring via management system.

## Slide 11: AC8000 – Optical node

## Slide 12: AC8000 – Inside view

## Slide 13: Node – Block diagram
Opt Receiver
Opt Transmitter

## Slide 14: AC8000 – Highlights
  Two or one plug-in forward receivers
  Two or one plug-in return transmitters
  One or two redundant power supplies
  2 active high level RF outputs, second output can be passively divided
  Plug-in diplex filters and adjustments
  Built-in ingress switches
  10 A remote power feeding / RF port (total 15 A)
  Housing dimensions (24 x 22 x 15) cm
  Upstream segmentation option
  Station memory for electrical identification
  Wide range of return laser technologies, e.g. 8 wavelength’s CWDM

## Slide 15: Device GUI – AC8000 Optical Node

## Slide 16: Spectrum analyser
Detailed Device GUI – AC8000 Optical Node

## Slide 17: User-Interface – US Monitoring: Ingress alarm

## Slide 18: User-Interface – US page

## Slide 19
Microprocessor deployment in the field applications 
Sensitive technology
Interfaces must be protected carefully
Strong signal port protection improves network reliability and uptimes – OPEX
Implemented in AC and CXE product lines
6 kV Surge Protection Approved according to EN61000-4-5

## Slide 20: Fibre to the Last Active - FttLA

## Slide 21: For FTTB applications
CXE800 optical receiver
      Economical small node in CXE housing
      Easy and fast installation
      Easy adjustment
      Reliable construction without any software
      High level RF output one or two ports
      Locally powered 220 VAC
      Without return transmitter

## Slide 22: CXE800 from inside

## Slide 24: FttH or RFoG nodes
  FTTH Node – RN1000
  Burst mode transmitter
  OLC function (-6…+1 dBm)
  One fibre solution
  ~ 80 dBµV RF output level
  DOCSIS 3.0 compatible
  Comply with SCTE 174

## Slide 25
Thank You
We build networks for the future