## Slide 1
Impact of LTE on the in-home installation
Premton Bogaj
Will CE class A screening be sufficient? A mathematical approximation.
Technical Solutions Specialist – South Eastern Europe

## Slide 2
Impact of LTE on the in-home installation
Agenda
LTE power versus screening effectiveness
Model
Calculating antenna gain from screening effectiveness
LTE impact at various distances
Screening effectiveness typical in-home components
Possible solutions
Conclusion

## Slide 3
Impact of LTE on the in-home installation
+
=
LTE transmitters:
handheld : +23dBm, antenna gain 0dB, EIRP = 200 mW
pico cell : +30dBm, antenna gain 5dB, EIRP = 3,2 W
macro cell : +46dBm, antenna gain 14dB, EIRP = 1000W (!!)
EIRP = Effective Isotropic Radiated Power = output power x antenna gain
Frequency 790 – 860 MHz
Screening effectiveness class A : 470-1000MHz > 75dB
?

## Slide 4
known:
* EIRP: Pt = output power x antenna gain [ W ]
*distance L [m]
Impact of LTE on the in-home installation
measure: Gri = antenna gain w.r.t. isotropic radiator
calculate:
calculate:
calculate:
( with λ being the used wavelength)
(with 120 π being the approximate impedance of free space)
for ρ use W/m2 and calculate injected voltage from the power with Z=75Ω

## Slide 5
Impact of LTE on the in-home installation
Screening effectiveness test using clamp method. Result is w.r.t. a dipole antenna.
Dipole antenna has a gain of +2,15 dBi w.r.t. an isotropic radiator.
Example: clamp test result of -75 dB (class A) equals an antenna gain of:
-75dB + 2,15dB = -72,85dBi =

## Slide 6
Impact of LTE on the in-home installation
EIRP = 200mW handheld LTE terminal
Screening effectiveness class A: 75dB
Aer = 5,9 · 10 -10 m²
frequency = 790 MHz ; λ = 0,38m
Distance LTE handheld / CATV component | Generated LTE field | Received power [W] | Injected LTE voltage Class A | Minimum screening effectiveness for 10dBµV injected voltage
0,5m | 4,8 V/m | 3,6· 10 -11 | 34 dBµV | 99 dB
1m | 2,4 V/m | 9,0· 10 -12 | 28 dBµV | 93 dB
3m | 0,8 V/m | 1,0· 10 -12 | 19 dBµV | 84 dB
6m | 0,4 V/m | 2,5· 10 -13 | 13 dBµV | 78 dB

## Slide 7
Impact of LTE on the in-home installation
EIRP = 1000W (60dBm = maximum macro cell) LTE base station
Screening effectiveness class A: 75dB
Aer = 5,9 · 10 -10 m²
frequency = 790 MHz ; λ = 0,38m
Distance LTE base station / CATV | Generated LTE field | Received power [W] | Injected LTE voltage class A | Minimum screening effectiveness for 10dBµV injected voltage
30m | 5,8 V/m | 5,2· 10-11 | 36 dBµV | 101 dB
60m | 2,9 V/m | 1,3· 10-11 | 30 dBµV | 95 dB
100m | 1,7 V/m | 4,7· 10-12 | 25,5 dBµV | 90,5 dB

## Slide 8
Impact of LTE on the in-home installation
quad-shield coax
F-connector splitter
Measured screening effectiveness
 75dB
 75dB

## Slide 9
Impact of LTE on the in-home installation
In-home amplifier
Wall outlet
Measured screening effectiveness
75dB
75dB

## Slide 10
Impact of LTE on the in-home installation
?
?

## Slide 11
Impact of LTE on the in-home installation
Testing with sniffers shows a significant
number of in-home networks
well below class A quality.
Calculating from measured field strength:
screening effectiveness of -40dB to -50dB
not uncommon.
Major cause: poor quality cable, cheap
connectors, very old wall outlets and
very old, poor quality amplifiers, bad
installation practice.
A bad installation could also compromise LTE reception….

## Slide 12
Use the best available in-home components with a screening effectiveness
>> class A.
Connectors are especially vulnerable. Make sure they are mounted and tightened
correctly. Use high quality connectorized leads where possible.
Susceptibility of the set top box or TV is unknown, this cannot be solved by
the customer.
The use of the LTE handheld on certain vulnerable spots in the home will lead to
problems that often cannot be controlled.
Impact of LTE on the in-home installation

## Slide 13
Impact of LTE on the in-home installation
Mathematical approximation to evaluate the impact of LTE handhelds in the
in-home installation
But…this is an approximation, the in-home environment is not an anechoic room
Class A alone is no guarantee that an LTE handheld will not generate
problems
Many currently used components however supersede class A performance
Set top box and TV are unknown risk factors
In many cases investment in the in-home installation will be necessary in order to
reduce the problems.
In some cases the problem might be very hard to pinpoint and control
if at all possible.

## Slide 14
Thank you!
premton.bogaj@technetix.com