## Slide 1: Towards delivering ultra high speed broadband services
Technical Division
Network and Services Planning and Developement Function
Dr Aleksandra Gajić
Notes: Hello, good morning. My name is Aleksandra Gajić, and I come from the incumbent company, Telekom Srbija, where I currently hold the position head of Section for fixed cable access network developement. As I understand the topic on this conference is mainly cable in the sense of coax, which we do not yet provide, but what I was planning to speak about is how to provide high speed and high quality services via the infrastructure that we do have, namely over copper and over fibre, and in which way do we, as a company, plan to compete with the evergrowing competition, namely the ones for whom this conference is actually tailored.

## Slide 2: Agenda
About us
Telekom Srbija broadband access network
Maximizing the potential of our network
Delivering high quality video, data and business services
Ongoing projects
Notes: And this is what I am planning to talk to you about today – I shall start with a short overview of our company, with which I am sure most of you are familliar of, but nevertheless, and then I would like to give a short overview of our existing infrastructure as well as of our plans for the future.
Please, do feel free to interrupt me at any time should you have some questions.

## Slide 3: About us

## Slide 4: Telekom Srbija Group
Telekom Srbija Group comprises the parent company Telekom Srbija a.d. and its subsidiary companies: Telekom Srpske a.d., m:tel d.o.o., Telus a.d., FiberNet d.o.o., TS:NET BV and HD WIN (Arena Sport TV channels).
The stake of Telekom Srbija a.d. in the capital of its subsidiaries as at 31 December 2012 amounts to the following:
Telekom Srpske a.d., Banja Luka 65%
m:tel d.o.o., Podgorica 51%
Telus a.d., Belgrade 100%
FiberNet d.o.o., Podgorica 100%
TS: NET BV, Amsterdam 100%
HD-WIN d.o.o 51%, Belgrade
Notes: Since its establishment, Telekom Srbija has looked among the visionary companies and entrepreneurs for the collaborators on the projects that followed the worldwide trends and imposed the national ones. Thus today part of the Telekom Srbija Group are Telekom’s subsidiaries: Telekom Srpske a.d., m:tel d.o.o., Telus a.d., Belgrade, FiberNet d.o.o., TS:NET BV and HD WIN (Arena Sport TV channels).

## Slide 5: Telekom Srbija brands
Notes: Our company developed in parallel with global trends, which resulted in the broadening of the range of telecommunications services that we offer our customers. Thus, at present, we provide fixed, mobile, Internet and multimedia services and a wide range of add-on services. A single name - Telekom Srbija – stands behind such market-proven brands and services as: mt:s, IPTV and Box
MTS – is the largest mobile operator in Serbia, synonymous with a customer’s friend, which has developed a business policy committed to the continuous expansion of services improving our customers’ everyday communication.
IPTV– is high-quality digital television, which, apart from its signal quality, crystal-clear image and sound, differs from traditional television in the method of distributing TV programmes. A top-quality interference-resistant digital signal reaches the users through Telekom Srbija’s network.
Box– is a brand which implies that mobile, fixed, Internet and TV services are integrated into a single offer. The Box primarily ensures cost reduction, i.e. additional savings and consolidation into a single invoice.

## Slide 6: Overview: Investments and customers
In million RSD | 2013 | Growth rate | 2012
Technical investments | 9.495 | -6,3% | 10.134
Infrastructural investments | 3.449 | 56,5% | 2.204
Total | 12.944 | 4,9% | 12.339
Chart: 
Switching and management system | 1637 | 1059
Access network | 2795 | 2155
Wireless network | 1483 | 2392
Transport optical network | 1734 | 1204
Internet and Multimedia | 1722 | 3141
Other technical invetments | 124 | 183
Notes: In order to retain the Telekom Srbija’s leading position in the Serbia’s telecommunications market, the investment was made in the amount of RSD 13 billion, which is 5% more than in the previous year.
The investments were made in technical development and creation of the network flexibility and reliability for regular operation of service platforms resulting in better quality of services ofered to our customers and in retaining the existing competitive advantage.
The Company allocated 73% of funds for investment in technical development of network, whereas 27% of total funds were invested in IT and logistics support.
In 2013 the development of technical investments was directed to the following activities:
In fixed telephony the investments were mainly intended for upgrade and eexpansion of access network providing the services on modern Broadband (BB) access to users. The network upgrade has eliminated the old systems and increased the number of users that have been offered modern and high-quality services. In 2013 digitalization reached 99.50% (in 2012 it was 99.11%).
In the Internet sphere, investments were directed towards expansion of the national IP/MPLS network and of the multiservice network. In 2013 the total number of ADSL ports increased by 7%, which resulted in an increase of free capacity by 12.5%.
In the sphere of multimedia, services were directed towards expansion of Headend and Middleware platforms.
As for investments in the technical capacities of the telecommunications network, most of the investments in 2013 by the Company were made in the access network (29%), Internet and multimedia (18%), transport optical network (18%), and switching management systems (17%) and wireless network (16%).

## Slide 7: Overview: Investments and customers
In thousands | 2013 | Growth rate | 2012
ADSL retail | 550 | 7.4% | 513
ADSL wholesale | 126 | -1.4% | 128
IPTV | 244 | 36.9% | 178
Web TV* | 20 | 24.0% | 16
Total | 941 | 12.7% | 835
Interenet and multimedia customers
*) No of subscriptions
Notes: Despite the challenges of growing competition, Telekom Srbija has a considerable number of customers in fixed and mobile telephony and an increasing number of Internet users.
The Internet market records growing customers’ demands for the Broadband Internet, which reflects the customer interest in the service enabling a high-quality and easily accessible content.
At the end of 2013, the Company had 550 thousand ADSL users in the retail segment, which accounts for 81% of the ADSL Internet market. Compared to the previous year, the Company recorded a 7.4% growth of ADSL users in retail.
In 2013, the number of IPTV users considerably increased (by 37%) as a result of the convergent packages offering. At the end of 2013, the Company had 244 thousand IPTV users.

## Slide 8: Telekom Srbija broadband access network

## Slide 9: Telekom Srbija – the development of BB
The development of BB in Telekom Srbija started in 2006. and since then the number of subscribers has increased significantly – from somewhat over a hundred thousand at the end of 2007 up to close to 730 thousand at the end of 2013.
Chart: 
| 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013
No of BB subscr. | 26215 | 133502 | 272761 | 409609 | 565636 | 639377 | 689122 | 732799
Notes: The development of BB started in 2006. and since then the number of subscribers has increased significantly – from somewhat over a hundred thousand at the end of 2007 up to close to 730 thousand at the end of 2013.

## Slide 10: FTTx architecture overview
Various types of FTTx architecture are deployed depending on location
FTTC for suburban and rural
FTTB for densely populated urban areas
FTTH for greenfield applications
1/3 of all the BB nodes are realized via mini IPAN equipment, mostly as FTTB
Notes: Together with the increasing number of subscribers, the offered services have become more and more bandwidth demanding, so the network architecture changed significantly as well.
Given that we are a major operator in the case of fixed telecommunications services, and as such have a large existing copper infrastructure that we feel the need to quickly and efficiently take advantage of, and yet at the same time we have to think about the high-speed bandwidths, our commitment naturally lies in fiber deployment. This conclusion can be derived by analyzing our current access network – it consists mostly of short local loops, the majority of which, close to 60%, is shorter than one kilometer, and as much as 85% is shorter than two kilometers, which is mostly places in cable ducts especially in urban areas. The average local loop length is somewhat above 1km, including uncongested rural areas. This represents a good basis in the cable as well in the infrastructural part.
In our current network we have more than one million xDSL ports installed, more than 150 thousand of which is VDSL2.
The large existing copper legacy pushes us to utilize it to its maximal potential, but at the same time we understand the need to prepare for the next step in which the bandwidths enabled by these copper loops will simply no longer suffice.
Bearing that in mid, we have installed access nodes in FTTC/B topology in more than 1000 locations in the past year and have ambitious plans to continue with such a decentralization and fiber deployment in the near future.

## Slide 11: Maximizing the potential of our network

## Slide 12: Deploying Network Analyzer
In order to enable proactive maintenance of the increasingly demanding access networks, it is necessary to apply appropriate network analyzing tools that will support operational best practices throughout the life cycle of the access lines - from planning, through service provisioning, maintenance, and up to troubleshooting and user support.
It is our goal to provide stable and high quality services by allowing remote diagnostic of the line quality and by acting proactively –addressing potential issues before they impact the customers
Rearranging line configuration parameters assures lines are working at their optimal performance
Notes: With higher speeds and the appearance of triple play services integrating voice, Internet access and video signal, as well as the significant growth of the number of our IPTV subscribers, the requirements that need to be met by the subscriber lines have tightened drastically. Same pairs are used on the very edge of their acquirable physical bit-rates, wherein the voice and video services require an increased stability in order to avoid an interruption of the signal and/or freezing of the video image or pixelization.
DSL technologies, such as ADSL and VDSL, allow these services to be provided to the end user in a more efficient way, but modern multimedia services are becoming more demanding in terms of bit rates, delay and the allowed number of errors, and thus become increasingly more sensitive to the quality of the line.
Problems arise with the occurrence of interference and crosstalk in copper pairs, which is manifested to the user as interference in the video signal, or when the service requirements exceed the capabilities that the line can achieve. In order to prevent interference, as well as to enable proactive maintenance of the increasingly demanding access networks, it is necessary to apply appropriate Network Analyzer software tools that will support operational best practices throughout the life cycle of the access lines - from planning, through the award of maintenance, and to solve problems and support users.

## Slide 13: Delivering high quality video, data and business services

## Slide 14: Delivering high speed broadband services
Enabling ultra-high speeds:
Migration to VDSL2 technology, since 2011
Maximizing the potential of our existing copper network - considering the deployment of cutting edge technologies such as vectoring in order to improve the DSL line performance
Providing our users with services efficiently tailored to measure by calculating the highest possible speed for each customer
CPE:
Expanding the competition among our CPE suppliers
Drastically lower the cost of the CPE devices
Different perspective regarding further network development
Setting the appropriate base for the future – vectoring capable/friendly CPE
Notes: In parallel with all the aforementioned activities, we have worked on expanding the competition among our CPE suppliers by which we have managed to drastically lower the cost of the CPE devices, which has led to an entirely different perspective of our network. The BBTF – IAD combination becomes much more cost effective, lowering the percentage of BB subscribers at which using two ports to provide dual or triple play services remains profitable. Also, it allows a quicker replacement of ADSL with VDSL services and permits higher numbers of vectoring capable equipment.

## Slide 15: Delivering high speed broadband services
Tests were performed on 36 different combinations of cable types, pair lengths, types of CPE equipment, profiles with various line speeds and with different mechanisms of protection against coding errors. The majority of these 36 cases showed an increase in line speed from 30% to 50%.
Vectoring trial:
Notes: Tests were performed on 36 different combinations of cable types, pair lengths, types of CPE equipment, profiles with various line speeds and with different mechanisms of protection against coding errors. The majority of these 36 cases showed an increase in line speed from 30% to 50%.
The application of vectoring reduced the differences in the line speeds and generally increased the speeds on each line individually
The greatest benefit from vectoring was noted at lengths between 300 and 700 m

## Slide 16: Ongoing projects

## Slide 17: Ongoing projects:
Deploying FTTB in a large number of locations in large cities – more than 1000 active nodes, another 1000 nodes planned in Q3 and Q4
FTTH deployment in greenfield locations
Broadening of the metro optical networks
Vectoring trial – maximizing the potential of our existing copper network
Migration towards the All IP concept

## Slide 18: … just to wrap it all up
Notes: Telecom's network architecture is something that is constantly improving and changing. Infrastructure that will be able to support high-quality and demanding broadband services involves the implementation of a large number of small access nodes, in the optimal locations in the network, which will allow the shortening of the copper subscriber loop that will lead to an improvement of their characteristics. A software tool which allows us to easily define those optimal spots in the network must also be able to adjust and adapt to the changing needs of the network architecture.
In addition, there is the possibility of line prequalification and segmentation based on their characteristics, which allows us to offer tailor-made services and features, while taking into account tat the line fulfills meets strict criteria so that the service provided be the highest quality possible.

## Slide 19: Thank you for your attention.